## Slide 1: Central Coast Long-term Environmental Assessment Network

## Slide 2
Mission
To Trace Sources, Loads and Effects of Contaminants in Ocean Waters along the Central California Coast
Established 2001

## Slide 3: Key Features
Participant-driven, adaptively managed program
  Program objectives
  Participants
  Governing structure
  Cost-sharing formula

## Slide 4: CCLEAN Program Objectives
1. Obtain high-quality data describing the status and long-term trends in the quality of Monterey Bay nearshore waters, sediments, and associated beneficial uses.
2. Determine whether Monterey Bay waters and sediments are in compliance with the Ocean Plan and associated NPDES permits.
3. Determine sources of contaminants to Monterey Bay nearshore waters.
4. Provide legally defensible data on the effects of wastewater discharges in Monterey Bay.

## Slide 5: CCLEAN Ancillary Goals
1. Manage adaptively to ensure cost effectiveness and response to emerging issues
2. Develop a long-term database on trends in the quality of Monterey Bay waters, sediments and associated beneficial uses.
3. Ensure that the database is compatible with other regional monitoring efforts and regulatory requirements.
4. Ensure that data are presented in ways that are understandable and relevant to the needs of stakeholders.

## Slide 6: Participants
City of Santa Cruz
City of Watsonville
Moss Landing Power Plant
Monterey Regional Water Pollution Control Agency
Carmel Area Wastewater District
California State Waterboard, Central Coast Region

## Slide 7: Governing Structure
Memorandum of Agreement
Simple governance style
  Single governing group (Steering Committee)
  Meets monthly
Senior technical staff or district managers
  Ability to make program revisions within regulatory limits

## Slide 8: Cost Sharing
Modest flat participation fee
Remainder of program costs divided according to running 5-year mean annual discharge volume

## Slide 9: Water Quality Stressors Sampled Under CCLEAN
Persistent Organic Pollutants (POPs) in water, sediments, and mussel tissues
Dissolved inorganic nutrients (ammonium, nitrate, phosphate, silicate)
Fecal Indicator Bacteria (FIBs: Enterococcus, total coliform, fecal coliform)

## Slide 10: POPs emphasized by CCLEAN
POP Group | Compounds measured
PAHs | Polynuclear aromatic hydrocarbons: Biphenyl, Naphthalene, 1-methylnapthalene, 2-methylnapthalene, 2,6-dimethylnapthalene, 2,3,5-trimethylnapthalene, Acenaphthene, Acenaphthylene, Anthracene, Dibenzothiophene, Fluorene, Phenanthrene, 1-methylphenanthrene, Benz(a)anthracene, Chrysene, Fluoranthene, Pyrene, Benzo(a)pyrene, Benzo(e)pyrene, Benzo(b)fluoranthene, Benzo(k)fluoranthene, Dibenz(a,h)anthracene, Perylene, Benzo(ghi)perylene, Indeno(1,2,3-cd)pyrene
DDTs | o,p’-DDT, p,p’-DDT = (1,1,1-trichloro-2,2-bis(p-chlorophenyl)ethane) o,p’-DDD, p,p’-DDD = (1,1-dichloro-2,2-bis(p-chlorophenyl)ethane) o,p’-DDE, p,p’-DDE = (1,1-dichloro-2,2-bis(p-chlorophenyl)ethylene)
Dieldrin | 1,2,3,4,10,10-hexachloro-6,7-epoxy-1,4,4α,5,6,7,8,8α-octahydro-1,4-endo,exo-5,8-dimethanonaphthalene
Chlordanes | trans-Chlordane, cis-Chlordane, trans-Nonachlor, cis-Nonachlor, Oxychlordane, Heptachlor, Heptachlor epoxide
Dioxins/Furans | TCDD, 2,3,7,8-; PeCDD, 1,2,3,7,8-; HxCDD, 1,2,3,4,7,8-; HxCDD, 1,2,3,6,7,8-; HxCDD, 1,2,3,7,8,9-; HpCDD, 1,2,3,4,6,7,8-; OCDD, 1,2,3,4,6,7,8,9-; TCDF, 2,3,7,8-; PeCDF, 1,2,3,7,8-; PeCDF, 2,3,4,7,8-; HxCDF, 1,2,3,4,7,8-; HxCDF, 1,2,3,6,7,8-; HxCDF, 1,2,3,7,8,9-; HxCDF, 2,3,4,6,7,8-; HpCDF, 1,2,3,4,6,7,8-; HpCDF, 1,2,3,4,7,8,9-

## Slide 11: POPs emphasized by CCLEAN
POP Group | Compounds measured
Pyrethroids | Allethrin, Bifenthrin, Cyfluthrin, Cyhalothrin - total lambda, Cypermethrin, Danitol (Fenpropathrin), Deltamethrin/Tralomethrin, Esfenvalerate, Fenvalerate, Fluvalinate, Permethrin-cis, Permethrin-trans, Tetramethrin
Fipronils | Fipronil, Fipronil desulfinyl, Fipronil sulfide, Fipronil sulfone
PCBs | congener numbers = all 209 congeners in water; congeners 5, 8, 18, 20, 21, 28, 31, 33, 43, 44, 49, 52, 56, 60, 61, 66, 69, 70, 73, 74, 76, 80, 86, 87, 89, 90, 93, 95, 97, 99, 101, 105, 106, 110, 111, 113, 115, 116, 117, 118, 127, 128, 132, 138, 139, 141, 147, 149, 151, 153, 156, 158, 160, 163, 164, 168, 170, 174, 177, 180, 181, 182, 183, 187, 190, 194, 195, 196, 201, 203 in tissues
PBDEs | Polybrominated diphenyl ethers: congener numbers = 7, 8, 10, 11, 12, 13, 15, 17, 25, 28, 30, 32, 33, 35, 37, 47, 49, 51, 66, 71, 75, 77, 79, 85, 99, 100, 105, 116, 119, 120, 126, 128, 138, 140, 153, 154, 155, 166, 181, 183, 190, 203, 206, 207, 208, 209

## Slide 12: Matrices and Sampling Frequency
Matrix | Parameters | Frequency
Rivers (San Lorenzo, Salinas, Pajaro, Carmel) | POPs, nutrients | Twice annually (wet and dry season)
Wastewater Effluent (Santa Cruz, Watsonville, Monterey, Carmel) | POPs, nutrients | Twice annually for POPs and weekly for nutrients
Monterey Bay receiving waters (Santa Cruz, Watsonville, Monterey) | FIBs | Monthly or weekly
Monterey Bay open waters (north and south) | POPs, nutrients, FIBs, TSS | Twice annually
Sediments and benthic fauna (6 sites along 80 m contour) | POPs, grain size, TOC | Annually in the dry season (sediments) and every 5 years (fauna)
Mussels (5 rocky intertidal sites) | POPs, lipid content | Annually in the wet season

## Slide 13: Sampling Locations

## Slide 14
Water Year
Monterey Bay POP concentrations 2001-2016

## Slide 15: Program Products
POP/nutrient load data
Comparison of sources
Concentrations of POPs in Monterey Bay
Special studies (physical oceanography, satellite Chlorophyll and nutrient loading)
Annual Reports – CCLEAN website
Downloadable data – CEDEN website

## Slide 16
http://www.cclean.org/

## Slide 18: Potential Links to CeNCOOS

## Slide 19: 1. Chlorophyll data
Association between nutrient loads from wastewater treatment plants and ocean chlorophyll concentrations

## Slide 20
Chlorophyll concentration time series data centered on wastewater discharge locations in Monterey Bay
Santa Cruz
Watsonville
Monterey
Carmel

## Slide 21: 2. Climate-related data
Examine relationship between factors, such as water temperature and pH, and decline in benthic infauna in Monterey Bay
Infauna

## Slide 22: 3. Particle trajectories
Date | River DDT (g/day) | Ocean DDT (ng/L)
Mar-2004 | 10.9 | 0.1691
Mar-2006 | 61.2 | 0.091
Mar-2007 | 21.5 | 0.076
Mar-2008 | 4.45 | 0.079
Mar-2009 | 10.7 | 0.099
Feb-2010 | 23.7 | 0.343
Mar-2011 | 95.7 | 0.029
Mar-2012 | 4.20 | 0.071
Apr-2013 | 0.402 | 0.104
Mar-2014 | 1.00 | 0.040
Mar-2015 | 1.25 | 0.035
Feb-2017 | 144.8 | 0.439
1Ocean Plan objective for DDT (0.17 ng/L) exceeded
Obtain particle trajectories from potential sources to our sampling locations